## Slide 1
COMPUTER ORGANIZATION & ASSEMBLY LANGUAGE
Traffic Light Control System
An Assembly Language Approach to Intelligent Intersection Management
Abdul Wahid (243699)
Ahmad Murtaza (243653)
Supervisor: Mam Anum Aftab

## Slide 2
PRESENTATION STRUCTURE
Contents
01
Project Overview
Introduction, objectives, and development environment
02
System Features
Core traffic control, monitoring, and pedestrian safety
03
Operational Modes
Normal, Emergency, Rush Hour, and Night modes
04
Technical Implementation
Hardware interface, signals, and timing systems
05
System Architecture
Program flow, phase sequence, and data structures
06
Testing & Results
Comprehensive validation and performance verification

## Slide 3
GETTING STARTED
Project Overview
Introduction
This project implements an intelligent traffic light control system using x86 Assembly language to manage four-way intersections with real-time monitoring and adaptive control.
The system demonstrates low-level programming, hardware interfacing, and embedded system design principles through a practical, real-world application.
Project Objectives
Implement multi-mode traffic control
Integrate pedestrian safety features
Provide real-time monitoring
Demonstrate hardware interface concepts
Enable emergency response capabilities
Development Environment
Language
x86 Assembly (8086)
Assembler
MASM / TASM
Platform
DOSBox Emulator
Hardware Interface
Port 4 (Traffic Light Control)
Memory Model
Small (.model small)

## Slide 4
CORE CAPABILITIES
System Features
Core Traffic Control
Multi-Directional Management
Independent North-South and East-West control
Synchronized signal transitions
All-red clearance phase between cycles
Signal States
NS Green
EW Red
All Yellow
Transition
EW Green
NS Red
All Red
Safety
Real-Time Monitoring
Live Countdown Timers
NS: 5s EW: 5s
Updates every second during green phases
Color-coded in green (0Ah) for visibility
Positioned at top-right corner of display
Statistics Dashboard
156
Cycle Counter
1,248
NS Cars
892
EW Cars
2/sec
Rate
Pedestrian Safety
Direction-Specific Signals
ALL CROSS
All-red phase only
NS CROSS / EW CROSS
Direction-specific green
STOP
Red signal warning
Manual Crossing Request
P
Key
Adds +3 seconds to current green phase
Auto-denied during inappropriate phases

## Slide 5
OPERATIONAL FLEXIBILITY
Operational Modes Overview
Normal Mode
Balanced Traffic Flow
Equal green time for all directions
5s
NS Green
5s
EW Green
2s
Yellow
5s
All Red
19s
Total Cycle
Default
Emergency Mode
Immediate Response
Clear path for emergency vehicles
All lights flash yellow (0.5s)
Continuous audio beeping
All traffic must stop
Key: E
Rush Hour Mode
Heavy Traffic Optimization
60% more green time for main road
8s
NS Green
3s
EW Green
3s
Yellow
3s
All Red
17s
Optimized Cycle
Key: R
Night Mode
Low-Traffic Operation
Reduce unnecessary waiting
All lights blink yellow (1s)
Treat as all-way stop
Proceed when safe
Key: M

## Slide 6
MODE 01
Normal Mode
19-Second Cycle Breakdown
0-5s
All Red
5-10s
NS Green
10-12s
All Yellow
12-17s
EW Green
17-19s
All Yellow
Key Characteristics
Balanced traffic flow for both directions
Equal green time distribution (5s each)
Standard transition timing (2s yellow)
Full pedestrian support with clear messages
Traffic Capacity
10
NS Cars / Cycle
10
EW Cars / Cycle
MODE 02
Emergency Mode
Purpose
Provide immediate response for emergency vehicles, ensuring rapid clearance of intersection traffic.
Activation Behavior
Flashing Lights
All lights flash yellow at 0.5s intervals
Audio Alert
Continuous beeping for attention
Traffic Protocol
All vehicles must stop immediately
Display Message
!!! EMERGENCY MODE ACTIVE - ALL TRAFFIC STOP !!!
Exit Command
N
Return to previous mode

## Slide 7
ADVANCED OPERATIONS
Rush Hour Mode & Night Mode
MODE 03
Rush Hour Mode
Timing Configuration Comparison
Phase | Normal | Rush Hour
NS Green | 5s | 8s (+60%)
EW Green | 5s | 3s (-40%)
Yellow | 2s | 3s
All Red | 5s | 3s
16
NS Cars / Cycle
vs 10 normal
6
EW Cars / Cycle
vs 10 normal
Key Benefits
Optimized for peak traffic on main roads
Improved traffic throughput efficiency
MODE 04
Night Mode
Purpose
Designed for low-traffic periods to minimize delays and reduce unnecessary idling.
Operational Behavior
Blinking Yellow
All lights blink at 1s intervals
All-Way Stop
Vehicles proceed when safe
0s
Timer Display
No countdown
D
Exit Command
Return to day

## Slide 8
UNDER THE HOOD
Technical Implementation
Hardware Interface
Output Port
Port 4
OUT 4, AX
16-Bit Pattern Structure
Bits 11-8
North-South Lights (RYG)
Bits 7-4
East-West Lights (RYG)
Signal Patterns
030Ch
NS Green
0861h
EW Green
0492h
All Yellow
0249h
All Red
0492h
Emergency
Video Memory Management
Memory Segment
0xB800
Direct access to video memory for fast rendering
Display Specifications
80×25
Text Mode
2 bytes
Per Char
Timing System
BIOS INT 15h (AH=86h)
MOV AL, 0 ; Critical for DOSBox
MOV CX, 000Fh ; High word
MOV DX, 4240h ; Low word (1s)
MOV AH, 86h
INT 15h
Custom Delay Procedures
DelayWithCountdown: All-red phase with beeps
DelayWithLiveTimer: Green phases with timer display

## Slide 9
SYSTEM DESIGN
System Architecture
Program Flow
START
Initialization
Main Loop
Phase Cycle
Check Modes
Keyboard Input
Emergency/Night Loop (if active)
Phase Sequence
19-Second Complete Cycle
Phase 0: All Red (0-5s)
NS: Red | EW: Red | Pedestrians: ALL CROSS
Phase 1: NS Green (5-10s)
NS: Green | EW: Red | Pedestrians: NS CROSS
Phase 2: All Yellow (10-12s)
NS: Yellow | EW: Yellow | Pedestrians: PREPARE STOP
Phase 3: EW Green (12-17s)
NS: Red | EW: Green | Pedestrians: EW CROSS
Phase 4: All Yellow (17-19s)
NS: Yellow | EW: Yellow | Pedestrians: PREPARE WALK
Data Structures
Mode Flags (DB)
emergency_mode DB 0
night_mode DB 0
rush_hour_mode DB 0
Timers & Counters
ns_timer DB 0
ew_timer DB 0
cycle_counter DW 0
Timing Configuration
ns_green_time DB 5
ew_green_time DB 5
yellow_time DB 2

## Slide 10
USER INTERACTION
User Controls & Interface
Keyboard Commands
Key | Function | Description
E | Emergency | Activate emergency mode
N | Normal | Exit emergency mode
P | Pedestrian | Request +3s crossing time
R | Rush Hour | Toggle rush hour mode
M | Night | Activate night mode
D | Day | Exit night mode
ESC | Exit | Terminate program
Features
Case-insensitive input
Real-time detection (INT 16h)
Immediate response
Mode validation before switching
Screen Layout
TRAFFIC CONTROL SYSTEM
============================

## Slide 11
VALIDATION & PERFORMANCE
Testing & Results
01
Normal Operation Test
✓ PASS
02
Emergency Mode Test
✓ PASS
03
Pedestrian Request Test
Phase | Request | Result
NS Green | Press P | ✓ +3s granted
Yellow | Press P | ✓ Denied
All Red | Press P | ✓ Denied
Emergency | Press P | ✓ Denied
04
Rush Hour Mode Test
05
Night Mode Test
✓ PASS
Overall Result
ALL TESTS PASSED
100% Success Rate
The system successfully validated all operational modes and edge cases, demonstrating robust performance and reliability.
✓ PASS

## Slide 12
PROJECT SUMMARY
Conclusion
Technical Achievements
Low-level hardware interface (Port 4)
Direct video memory manipulation
Efficient timing using BIOS interrupts
Real-time input processing
Multi-mode state management
Functional Features
Four operational modes
Pedestrian safety system
Real-time monitoring
Emergency response capability
Adaptive timing (rush hour)
Learning Outcomes
Mastered x86 Assembly programming
Understood hardware communication
Learned real-time system design
Implemented state machine logic
Applied traffic engineering concepts
Real-World Applicability
This system simulates actual traffic management principles and can serve as a foundation for embedded traffic control systems. The modular design allows for easy expansion and modification, demonstrating practical applications of low-level programming in critical infrastructure systems.
Developed by
Abdul Wahid & Ahmad Murtaza